Document # HW0001

	Adaptec Host Adapter Hardware Commonly Asked Questions  3/93


	Q.  Why does my computer/SCSI HA think that I have 7 hard drives,
	(or CD-ROMs, or ..) when I only have one drive connected?

	A.  When installing an Adaptec SCSI HA, SCSI bus protocol must
	be observed.  The HA should be SCSI ID 7, always the highest ID
	number, so that the HA will always win SCSI bus arbitration.
	SCSI bus theory dictates that each device (the HA is a device)
	must have a unique and separate SCSI ID number.  If a HD or
	other device is attached to the SCSI bus with the same ID as the HA, 
	then the HA will see a response for "phantom" devices at IDs where no 
	device exists.  To solve this problem, simply set the devices ID to 
	something other than that of the HAs SCSI ID.  If the device is a 
	boot drive, then the SCSI ID should be set at 0.  
	
	The 152x/154xB/1640/174x (in standard mode) BIOS controls hard drives 
	at SCSI ID 0 and 1 only.  
	The 174x BIOS in enhanced mode will control hard drives at SCSI ID's 0
	through 6.  Hard drives or SCSI devices using ID's 2 through 6
	need device drivers to be controlled using the 152x/154xB/1640 or
	174x in standard mode.


	Q.  Why can't I use the entire size of my hard drive that is 
	rated over 1 Gigabyte in capacity, when I am using DOS?

	A.  DOS 4.x and above has a limitation of 1024 cylinders per
	physical drive.  This limitation, on current disk controllers
	and SCSI HAs that utilize the standard of 1 Megabyte per 
	cylinder, leads to a 1 Gigabyte limit.  Only our 1542B/GIG and
	174xA (with special BIOS in Enhanced Mode using ASW-C174 v3.1) 
	have the ability to break this limit.
	If your 154xB has a BIOS part number of 420418-00D
	or greater, or if your 174xA has a BIOS part number of 
	450216-00-A or greater, then you already have support for more 
	than 1 Gigabyte.  Refer to your User's Manual addendum for help 
	on setting up this feature.  Alternatively users
	who need this support can download the latest 154xB or 174x 
	microcode/BIOS files from this BBS for use with an EPROM burner. 
	The EPROMs needed are 27C128 at 200ns for the 154xB and 150ns
	for the 174x.  154xC boards come ready to support hard drives
	larger that 1 Gigabyte.


	Q.  Why can't I use my new CD-ROM/Tape/WORM drive with my 
	Adaptec HA?

	A.  Most Adaptec SCSI HAs are designed to support two HDs and 
	on some models 2 floppy drives with just a bare board.  Additional
	devices require the use of a device driver.
	For more information on what your particular HA/kit should support, 
	contact your dealer/distributor or look at KITS.TXT on this BBS 
	for an overview.  Spec sheets are available on Adaptec's Interactive
	FAX system.


	Q.  Why when I boot do I see a message that says
	something like "SCSI BIOS not installed", or I see a message that
	says "Drive C already installed" or "Searching for Target 0"
	and my computer hangs here for about 60 seconds before going
	on?

	A.  The BIOS on Adaptec HAs is used primarily for booting off 
	of attached SCSI HDs set to ID 0 (Target 0).  SCSI ID of the HD
	is set with jumpers or switches located on the HD.  
	If the HA you are using is not being used to control a bootable 
	SCSI HD, and the HA has been working with the attached devices 
	and their associated drivers, then disable the BIOS on the HA 
	you are using.  Consult your HA User's Guide, or Installation 
	Pamphlet for the jumper that enables the BIOS, or the software 
	switch that needs to be set to disable the BIOS.  152x and 154x 
	boards can have the BIOS disabled with jumpers, 1640 and 174x 
	boards BIOS' enabling is controlled by software.  The 154xC
	board's BIOS address is controlled by DIP switched located at the
	top edge of the board.


	Q.  Why does my 174x board always come up in the configuration
	as being in Standard Mode, and what is the difference between
	Standard Mode and Enhanced Mode?

	A.  The default of the configuration files and overlay files used
	to configure the 174x is the most compatible mode, Standard.
	Standard Mode is equivalent to 154x emulation.  Standard Mode
	requires IRQ, DMA and I/O port definitions and policing by the
	installer.  Only 4 174x's can be used if all are in Standard mode 
	because of the number of available DMA channels for use in this mode.
	Enhanced Mode allows the installer the luxury of not having to 
	worry about the DMA, IRQ and I/O address, as this is all taken 
	care of by the configuration and EISA motherboard.  Enhanced mode
	also is the only mode that supports Fast-SCSI (up to 10 Meg/sec.
	and 32 bit addressing).  
	Up to 4 Gig of RAM is supported, with up to 12 HAs being allowed,
	with the limit being imposed by the number of EISA slots.
	Standard BIOS supports 2 hard drives with support for more hard
	drives or other device types coming from device drivers.  
	Standard BIOS requires the use of ASPI4DOS.SYS for DOS ASPI management.
	Enhanced BIOS supports up to 7 hard drives of up to 8 Gigabyte
	each, with support for other devices coming from device drivers.
	Enhanced BIOS requires the use of ASPIEDOS.SYS for DOS ASPI management.
	Support for drives grater than one Gigabyte can only be achieved with
	174x BIOS part number 450216-00A or greater with the ASW-C174
	version 3.1 configuration files, available on this BBS in the
	file called ASWC174.EXE.  As with any Adaptec host adapter,
	hard drives controlled by the BIOS need to be partitioned with
	DOS's FDISK for use with DOS.

	Q.  Why can't I configure my 174x in Enhanced Mode, seeing
	the EISA motherboard error "ID mismatch in slot X", or why
	do I always see the error "Host Adapter Initialization Failed!"
	when I configure the card for Enhanced Mode?

	A.  As the EISA standard evolved,  the 
	differences between different manufacturers propagated.  The
	174x family of boards are well designed, high performance boards
	that need some special attention to get them installed in a 
	few EISA motherboards.  Some of the Adaptec Technical Support
	situations that have occurred include:

	     1) When using the AMI ECU program, the installer should 
		verify that they are using version 1.4C or higher of 
		that ECU program.  When using this ECU program, the 
		installer should verify that they are using the 
		correct CFG file needed for their type of 174x
		board, and that the file ADP0000.OVR (dated 6/4/92) 
		exists in the same directory that the ECU
		program and CFG files are in.  When using the AMI ECU
		program earlier than 1.4C, the installer will not be
		able to configure the board in Enhanced Mode, using
		the ASW-C174 utilities v3.0 or later.  
		To configure the 174x, put the appropriate !ADPxxxx.CFG
		file from the ASW-C174 configuration set into the same
		directory that the CFG.EXE program is run from.
		The files are:
			!ADP0000.CFG            AHA-1740 (no letter)
			!ADP0001.CFG            AHA-1740A
						or AHA-1742A w/floppy 
								disabled
			!ADP0002.CFG            AHA-1742A
			!ADP0400.CFG            AHA-1744
		Also, in the same directory, be sure that the 
		ADP0000.OVR file exists.

	     2) When using some Compaq DeskPro, SystemPro, or similar 
		computers that have the CPU mounted on a special board, the
		installer should take care to minimize the number
		of boards between the CPU board and the Adaptec
		174x board.  It seems that when other EISA boards
		exist between the Adaptec HA and the CPU board, the
		Enhanced Mode configuration will not complete, or
		the board will report an error indicating that the
		HA could not be initialized.  This seems to be a
		situation that is not consistent, and is usually only
		associated with EISA communication boards in the
		slots between the HA and CPU boards.

	     3) It seems that some 50Mhz and faster motherboards have
		increased the response time of the INT signal from
		the adapter cards.  If your 50MHz or faster
		EISA motherboard gives you the error "Failed to 
		Initialize Host Adapter" after configuring it for
		Enhanced Mode, then follow these steps.
		Using a DOS editor, open the CFG file (it's ASCII text)
		being used.  Somewhere around line 120 you will see a line that
		reads "CHOICE = ENHANCED MODE".  Under this a few lines
		will be the line "TRIGGER = EDGE" or "TRIGGER = LEVEL".
		If this line says EDGE, change EDGE to LEVEL, this is the
		standard setting for MOST EISA motherboards.  If it
		says LEVEL, then try using EDGE.  
		WARNING!!!  This fix has only been used in less than
		one percent of the cases, so don't use this as a catch all
		fix.  The recommended and default setting is LEVEL.